## Slide 1
Ultrasound Measurement of the Optic Nerve Sheath Diameter for Bedside Detection of Elevated Intracranial Pressure
Benjamin R. Tellier PA-SIII and Patrick Loftis, PA-C, MPAS, Clinical Associate Professor
Marquette University College of Health Sciences Physician Assistant Program
In adult patients with suspected eICP, is transorbital ultrasound measurement of the optic nerve sheath diameter (ONSD) as accurate as invasive ICP monitoring (intraventricular pressure monitoring or intraparenchymal pressure monitoring) for determining eICP?
Clinical Question for Evidence Based Literature Review
OVID Medline was used as the primary search database, and the search was conducted on 8/06/2018. MESH terms were organized for maximal inclusion and were organized into injury/outcome, intervention, target, and comparison terms.
Injury/outcome MESH terms included: Brain injuries, Traumatic Brain Injuries, Craniocerebral Trauma, Intracranial Hypertension, elevated Intracranial Pressure, intracranial pressure, Cerebrospinal Fluid Pressure, Intracranial Hemorrhages, and Brain Edema.
Intervention MESH terms were ultrasound and ultrasonography.
Target MESH terms included: optic nerve, myelin sheath, and optic nerve sheath diameter.mp.
Comparison MESH term was physiologic monitoring, invasive intracranial pressure monitoring.mp, intracranial pressure monitoring.mp, and external ventricular device.mp.
The Injury/Outcome, Intervention, Target, and Comparison terms—previously combined with the Boolean operator “or”—were combined with the Boolean Operator “and.” The search was limited according to articles published between 2011 and 2018. The search was limited to English language, humans, and “all adult (19 plus years)”. This search yielded 8 articles.
Pubmed was also used on 8/06/2018 as a secondary database. The search strategy was like the previous with some minor adjustments (see Appendix 1). This search produced 26 unique results.
Web of Science was also used on 8/06/2018 as a tertiary database. The search strategy was like the previous with some minor adjustments (see Appendix 2). This search produced 64 unique results.
Inclusion Criteria: contained adult patients, looked at eICP as an outcome, compared ultrasound measurement of ONSD to the gold standard invasive intracranial monitoring (intraparenchymal pressure monitoring or intraventricular pressure monitoring)
Exclusion Criteria: review articles, systematic reviews, meta-analysis articles, articles without eICP as an outcome measure, measurement of ONSD, use of gold standard comparisons, <15 subjects in the study, or PICO questions not aligned with the study question. Also, articles were excluded because they contained non-human, pediatric, pregnant, and brain-dead patients or cadavers.
Methodology
Abstract
Background: Elevated intracranial pressure (eICP) is a potentially fatal complication of intracranial pathology and rapid recognition is key. Invasive pressure monitors are the current gold standard, but this may be delayed, unavailable, or contraindicated. Ultrasound is a non-invasive, inexpensive, and rapid assessment tool that is becoming more widely available and can be performed bedside. Still, the question remains: In adult patients with suspected eICP, is transorbital ultrasound measurement of the optic nerve sheath diameter (ONSD) as accurate as invasive ICP monitoring (intraventricular pressure monitoring or intraparenchymal pressure monitoring) for determining eICP?
Methods: OVID Medline, Pubmed, and Web of Science were used as search databases. Final search was conducted on 8/06/2018. MESH terms were organized for maximal inclusion and were organized into injury/outcome, intervention, target, and comparison terms. 103 total articles were found, but only 6 articles were designated for critical appraisal after meeting inclusion criteria and not containing exclusion criteria.
Results: 304 total patients were included across 6 studies from multiple geographic regions. Optimal ONSD cutoff ranged from 4.8 to 5.85mm across all included studies. Sensitivity included values from 82.6% to 98%. Specificity varied from 80.4% to 100%. Positive predictive value values ranged from 53% to 100%. Negative predictive value included values ranging from 95.5% to 100%.
Discussion and Conclusion: In adult patients with suspected eICP, transorbital ultrasound measurement of ONSD correlates with the gold standard, is sensitive and specific, and is superior to other non-invasive methods to monitor and detect immediate changes in ICP. However, this technique requires additional meta-analysis and study to more thoroughly validate the technique and establish an optimal ONSD cutoff value that is representative of a multi-ethnic population.
.
In adult patients with suspected eICP, transorbital ultrasonography of the ONSD is an accurate, rapid, and cost-effective method for detecting eICP. ONSD measurements correlate with the gold standard, are sensitive and specific, can detect immediate changes in ICP, and are superior to other non-invasive methods of ICP monitoring.
-Therefore, it might be a useful tool when invasive ICP monitoring is delayed, unavailable, or contraindicated, in hospitals without neurosurgical services, or in rural or resource-limited settings.
-All of the studies utilized sample populations at either one or two medical centers, limiting applicability of the results. This is despite how studies were performed in multiple countries and on multiple ethnic groups.
So, there is ample opportunity to conduct the first blinded large scale multi-center controlled prospective cohort trial
Conclusion
References
Frumin E, Schlang J, Wiechmann W, et al. Prospective Analysis of Single Operator Sonographic Optic Nerve Sheath Diameter Measurement for Diagnosis of Elevated Intracranial Pressure. West J Emerg Med. 2014;15(2):217-220. doi: 10.5811/westjem.2013.9.16191.
Jeon JP, Lee SU, Kim SE, et al. Correlation of Optic Nerve Sheath Diameter with Directly Measured Intracranial Pressure in Korean Adults Using Bedside Ultrasonography. PLoS One. 2017;12(9):e0183170. doi: 10.1371/journal.pone.0183170.
Maissan IM, Dirven, Perjan J A C, Haitsma IK, Hoeks SE, Gommers D, Stolker RJ. Ultrasonographic Measured Optic Nerve Sheath Diameter as an Accurate and Quick Monitor for Changes in Intracranial Pressure. J Neurosurg. 2015;123(3):743-747. doi: 10.3171/2014.10.JNS141197.
Raffiz M, Abdullah JM. Optic Nerve Sheath Diameter Measurement: A Means of Detecting Raised ICP in Adult Traumatic and Non-Traumatic Neurosurgical Patients. Am J Emerg M. 2016;35(1):150-153. doi: 10.1016/j.ajem.2016.09.044.
Rajajee V, Vanaman M, Fletcher J, Jacobs T. Optic Nerve Ultrasound for the Detection of Raised Intracranial Pressure. Neurocrit Care. 2011;15(3):506-515. doi: 10.1007/s12028-011-9606-8.
Robba C, Cardim D, Tajsic T, et al. Ultrasound Non-Invasive Measurement of Intracranial Pressure in Neurointensive Care: A Prospective Observational Study. PLoS medicine. 2017;14(7):e1002356. doi: 10.1371/journal.pmed. 1002356.
The purpose of is to review literature published since 2011 on determination of eICP by ultrasound measurement of optic nerve sheath diameter ONSD, compared to the invasive ICP monitors, in adult patients.
Purpose of Literature Review
Image obtained from http://casemed.case.edu/clerkships/neurology/NeurLrngObjectives/Monroe%20Kellie.htm
The best available evidence supports variable sensitivity and specificity with the presence of a moderate12, 16,17 to large13, 14, 15 correlation between ultrasound measurement of ONSD and invasive ICP monitoring for the detection of eICP. 304 total patients were included across 6 studies from multiple geographic regions and ethnic populations.
Optimal ONSD cutoff to be between 4.8mm16and 5.85mm17
Sensitivity ranges from 82.6%17 to 98%16
Specificity ranges from 80.4%15 to 100%12
Positive predictive value ranges from 53%16 to 100%12
Negative predictive value ranges from 95.5%12 to 100%16
Results
Image obtained from https://www.nature.com/articles/jhh201512
Study size- limiting factor in external validity with all studies containing between 24 and 65 patients.
Single vs multiple sonographers- Only one study12 used a single experienced sonographer to eliminate this as a confounding variable, thus some of the variability in correlation, sensitivity, specificity, and ONSD cutoff value may be due to inexperienced sonographers or lack of proficiency with the technique.
No current established non-pathologic ONSD value average for the general population or any specific ethnic group.
Discussion